## Slide 1
COPYOF DESCENT-4-35-170.145

## Slide 2: Table of Contents
Geometry and Mesh
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Report Definitions
Plots
  Residuals
  Report Plots

## Slide 3
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 4
Table of contents
Simulation Setup
Simulation Setup

## Slide 5
Table of contents
Simulation Setup / Physics
Physics

## Slide 6: Models
Model | Settings
Space | 3D
Time | Steady
Viscous | SST k-omega turbulence model
Table of contents
Simulation Setup / Physics / Models

## Slide 7: Material Properties
- Fluid | 
- air | 
Density | 1.225 kg/m^3
Cp (Specific Heat) | 1006.43 J/(kg K)
Thermal Conductivity | 0.0242 W/(m K)
Viscosity | 1.7894e-05 kg/(m s)
Molecular Weight | 28.966 kg/kmol
- Solid | 
- aluminum | 
Density | 2719 kg/m^3
Cp (Specific Heat) | 871 J/(kg K)
Thermal Conductivity | 202.4 W/(m K)
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 8: Cell Zone Conditions
- Fluid | 
- solid | 
Material Name | air
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Laminar zone? | no
Porous zone? | no
3D Fan Zone? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions

## Slide 9: Boundary Conditions
- Inlet | 
- inlet | 
Velocity Specification Method | Magnitude, Normal to Boundary
Reference Frame | Absolute
Velocity Magnitude [m/s] | 170.145
Supersonic/Initial Gauge Pressure [Pa] | 0
Turbulent Specification Method | Intensity and Viscosity Ratio
Turbulent Intensity [%] | 5
Turbulent Viscosity Ratio | 10
- Outlet | 
- outlet | 
Backflow Reference Frame | Absolute
Gauge Pressure [Pa] | 0
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 3)

## Slide 10: Boundary Conditions
Pressure Profile Multiplier | 1
Backflow Direction Specification Method | Normal to Boundary
Turbulent Specification Method | Intensity and Viscosity Ratio
Backflow Turbulent Intensity [%] | 5
Backflow Turbulent Viscosity Ratio | 10
Backflow Pressure Specification | Total Pressure
Build artificial walls to prevent reverse flow? | no
Radial Equilibrium Pressure Distribution | no
Average Pressure Specification? | no
Specify targeted mass flow rate | no
- Wall | 
- walls | 
Wall Motion | Stationary Wall
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 3)

## Slide 11: Boundary Conditions
Shear Boundary Condition | No Slip
Wall Surface Roughness | rough bc standard
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
- wing | 
Wall Motion | Stationary Wall
Shear Boundary Condition | No Slip
Wall Surface Roughness | rough bc standard
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 3)

## Slide 12: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Enthalpy | 0 J/kg
Length | 1 m
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 13: Solver Settings
- Equations | 
Flow | True
Turbulence | True
- Numerics | 
Absolute Velocity Formulation | True
- Pseudo Time Explicit Relaxation Factors | 
Density | 1
Body Forces | 1
Turbulent Kinetic Energy | 0.75
Specific Dissipation Rate | 0.75
Turbulent Viscosity | 1
Explicit Momentum | 0.5
Explicit Pressure | 0.5
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 14: Solver Settings
- Pressure-Velocity Coupling | 
Type | Coupled
Pseudo Time Method (Global Time Step) | True
- Discretization Scheme | 
Pressure | Second Order
Momentum | Second Order Upwind
Turbulent Kinetic Energy | Second Order Upwind
Specific Dissipation Rate | Second Order Upwind
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 15: Solver Settings
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-14
Minimum Spec. Dissipation Rate [s^-1] | 1e-20
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 16: Run Information
Number of Machines | 1
Number of Cores | 12
Case Read | 19.191 seconds
Iteration | 12.335 seconds
AMG | 6.974 seconds
Virtual Current Memory | 2.51395 GB
Virtual Peak Memory | 2.94292 GB
Memory Per M Cell | 65.3601
Table of contents
Run Information

## Slide 17: Solution Status Iterations: 65
 | Value | Absolute Criteria | Convergence Status
continuity | 0.0009965878 | 0.001 | Converged
x-velocity | 1.881801e-08 | 0.001 | Converged
y-velocity | 1.063124e-09 | 0.001 | Converged
z-velocity | 1.398543e-09 | 0.001 | Converged
k | 0.0001473185 | 0.001 | Converged
omega | 1.111328e-05 | 0.001 | Converged
Table of contents
Solution Status

## Slide 18: Report Definitions
lift_force | 19649.09 | N
drag_force | 1790.361 | N
Table of contents
Report Definitions

## Slide 19
Table of contents
Plots
Plots

## Slide 20: Residuals
Chart: Residuals
Table of contents
Plots / Residuals

## Slide 21
Table of contents
Plots / Report Plots
Report Plots

## Slide 22: drag_force-rplot
Chart: drag_force-rplot
Table of contents
Plots / Report Plots / report plots

## Slide 23: lift_force-rplot
Chart: lift_force-rplot
Table of contents
Plots / Report Plots / report plots