## Slide 1
TAKEOFF-3-45-102.087

## Slide 2: Header
Analyst | GADDALA CHETAN
Date | 12/10/2024 08:52 PM
Table of contents

## Slide 3: Table of Contents
System Information
Geometry and Mesh
  Mesh Size
  Mesh Quality
  Orthogonal Quality
Simulation Setup
  Physics
    Models
    Material Properties
    Cell Zone Conditions
    Boundary Conditions
    Reference Values
  Solver Settings
Run Information
Solution Status
Report Definitions
Plots
  Residuals
  Report Plots

## Slide 4: System Information
Application | Fluent
Settings | 3d, double precision, pressure-based, SST k-omega
Version | 24.1.0-10184
Source Revision | 5b3f9fb3c8
Build Time | Nov 22 2023 10:32:41 EST
CPU | 12th Gen Intel(R) Core(TM) i5-12450H
OS | Windows
Table of contents
System Information

## Slide 5
Table of contents
Geometry and Mesh
Geometry and Mesh

## Slide 6: Mesh Size
Cells | Faces | Nodes
29984 | 191312 | 156299
Table of contents
Geometry and Mesh / Mesh Size

## Slide 7: Mesh Quality
Name | Type | Min Orthogonal Quality | Max Aspect Ratio
solid | Poly Cell | 0.24020138 | 18.707652
Table of contents
Geometry and Mesh / Mesh Quality

## Slide 8: Orthogonal Quality
Table of contents
Geometry and Mesh / Orthogonal Quality

## Slide 9
Table of contents
Simulation Setup
Simulation Setup

## Slide 10
Table of contents
Simulation Setup / Physics
Physics

## Slide 11: Models
Model | Settings
Space | 3D
Time | Steady
Viscous | SST k-omega turbulence model
Table of contents
Simulation Setup / Physics / Models

## Slide 12: Material Properties
- Fluid | 
- air | 
Density | 1.225 kg/m^3
Cp (Specific Heat) | 1006.43 J/(kg K)
Thermal Conductivity | 0.0242 W/(m K)
Viscosity | 1.7894e-05 kg/(m s)
Molecular Weight | 28.966 kg/kmol
- Solid | 
- aluminum | 
Density | 2719 kg/m^3
Cp (Specific Heat) | 871 J/(kg K)
Thermal Conductivity | 202.4 W/(m K)
Table of contents
Simulation Setup / Physics / Material Properties

## Slide 13: Cell Zone Conditions
- Fluid | 
- solid | 
Material Name | air
Specify source terms? | no
Specify fixed values? | no
Frame Motion? | no
Laminar zone? | no
Porous zone? | no
3D Fan Zone? | no
Table of contents
Simulation Setup / Physics / Cell Zone Conditions

## Slide 14: Boundary Conditions
- Inlet | 
- inlet | 
Velocity Specification Method | Magnitude, Normal to Boundary
Reference Frame | Absolute
Velocity Magnitude [m/s] | 102.087
Supersonic/Initial Gauge Pressure [Pa] | 0
Turbulent Specification Method | Intensity and Viscosity Ratio
Turbulent Intensity [%] | 5
Turbulent Viscosity Ratio | 10
- Outlet | 
- outlet | 
Backflow Reference Frame | Absolute
Gauge Pressure [Pa] | 0
Table of contents
Simulation Setup / Physics / Boundary Conditions (1 of 3)

## Slide 15: Boundary Conditions
Pressure Profile Multiplier | 1
Backflow Direction Specification Method | Normal to Boundary
Turbulent Specification Method | Intensity and Viscosity Ratio
Backflow Turbulent Intensity [%] | 5
Backflow Turbulent Viscosity Ratio | 10
Backflow Pressure Specification | Total Pressure
Build artificial walls to prevent reverse flow? | no
Radial Equilibrium Pressure Distribution | no
Average Pressure Specification? | no
Specify targeted mass flow rate | no
- Wall | 
- walls | 
Wall Motion | Stationary Wall
Table of contents
Simulation Setup / Physics / Boundary Conditions (2 of 3)

## Slide 16: Boundary Conditions
Shear Boundary Condition | No Slip
Wall Surface Roughness | rough bc standard
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
- wing | 
Wall Motion | Stationary Wall
Shear Boundary Condition | No Slip
Wall Surface Roughness | rough bc standard
Wall Roughness Height [m] | 0
Wall Roughness Constant | 0.5
Table of contents
Simulation Setup / Physics / Boundary Conditions (3 of 3)

## Slide 17: Reference Values
Area | 1 m^2
Density | 1.225 kg/m^3
Enthalpy | 0 J/kg
Length | 1 m
Pressure | 0 Pa
Temperature | 288.16 K
Velocity | 1 m/s
Viscosity | 1.7894e-05 kg/(m s)
Ratio of Specific Heats | 1.4
Yplus for Heat Tran. Coef. | 300
Reference Zone | solid
Table of contents
Simulation Setup / Physics / Reference Values

## Slide 18: Solver Settings
- Equations | 
Flow | True
Turbulence | True
- Numerics | 
Absolute Velocity Formulation | True
- Pseudo Time Explicit Relaxation Factors | 
Density | 1
Body Forces | 1
Turbulent Kinetic Energy | 0.75
Specific Dissipation Rate | 0.75
Turbulent Viscosity | 1
Explicit Momentum | 0.5
Explicit Pressure | 0.5
Table of contents
Simulation Setup / Solver Settings (1 of 3)

## Slide 19: Solver Settings
- Pressure-Velocity Coupling | 
Type | Coupled
Pseudo Time Method (Global Time Step) | True
- Discretization Scheme | 
Pressure | Second Order
Momentum | Second Order Upwind
Turbulent Kinetic Energy | Second Order Upwind
Specific Dissipation Rate | Second Order Upwind
- Solution Limits | 
Minimum Absolute Pressure [Pa] | 1
Maximum Absolute Pressure [Pa] | 5e+10
Minimum Static Temperature [K] | 1
Maximum Static Temperature [K] | 5000
Table of contents
Simulation Setup / Solver Settings (2 of 3)

## Slide 20: Solver Settings
Minimum Turb. Kinetic Energy [m^2/s^2] | 1e-14
Minimum Spec. Dissipation Rate [s^-1] | 1e-20
Maximum Turb. Viscosity Ratio | 100000
Table of contents
Simulation Setup / Solver Settings (3 of 3)

## Slide 21: Run Information
Number of Machines | 1
Number of Cores | 12
Case Read | 19.594 seconds
Iteration | 10.741 seconds
AMG | 6.014 seconds
Virtual Current Memory | 1.29071 GB
Virtual Peak Memory | 3.46304 GB
Memory Per M Cell | 40.6953
Table of contents
Run Information

## Slide 22: Solution Status Iterations: 57
 | Value | Absolute Criteria | Convergence Status
continuity | 0.000943266 | 0.001 | Converged
x-velocity | 1.375143e-08 | 0.001 | Converged
y-velocity | 1.36106e-09 | 0.001 | Converged
z-velocity | 1.233996e-09 | 0.001 | Converged
k | 0.000111994 | 0.001 | Converged
omega | 1.299765e-05 | 0.001 | Converged
Table of contents
Solution Status

## Slide 23: Report Definitions
lift_force | 7598.426 | N
drag_force | 676.8625 | N
Table of contents
Report Definitions

## Slide 24
Table of contents
Plots
Plots

## Slide 25: Residuals
Chart: Residuals
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0 | 53.0 | 54.0 | 55.0 | 56.0 | 57.0
continuity | 1 | 1 | 1 | 1 | 0.93144 | 0.83646 | 0.73073 | 0.62891 | 0.5351 | 0.45095 | 0.37556 | 0.31389 | 0.25578 | 0.21054 | 0.17161 | 0.13984 | 0.11571 | 0.099064 | 0.088755 | 0.086179 | 0.089507 | 0.096711 | 0.10604 | 0.11509 | 0.12258 | 0.12687 | 0.128 | 0.12614 | 0.12142 | 0.11418 | 0.10552 | 0.095814 | 0.085656 | 0.075457 | 0.065645 | 0.056396 | 0.047832 | 0.040117 | 0.033383 | 0.027566 | 0.022611 | 0.018426 | 0.014961 | 0.012102 | 0.0097697 | 0.0078659 | 0.0063355 | 0.0050983 | 0.0041158 | 0.0033291 | 0.002716 | 0.0022232 | 0.0018394 | 0.0015294 | 0.0012896 | 0.0010941 | 0.00094327
x-velocity | 1.8565e-05 | 1.6821e-05 | 1.5635e-05 | 1.4163e-05 | 1.2513e-05 | 1.0795e-05 | 9.1304e-06 | 7.5838e-06 | 6.2307e-06 | 5.0632e-06 | 4.1042e-06 | 3.3276e-06 | 2.6955e-06 | 2.2116e-06 | 1.8542e-06 | 1.6079e-06 | 1.4667e-06 | 1.4283e-06 | 1.498e-06 | 1.6606e-06 | 1.8861e-06 | 2.1202e-06 | 2.3198e-06 | 2.4602e-06 | 2.5276e-06 | 2.5197e-06 | 2.4416e-06 | 2.3062e-06 | 2.1283e-06 | 1.9167e-06 | 1.7007e-06 | 1.4875e-06 | 1.2833e-06 | 1.0935e-06 | 9.2102e-07 | 7.6775e-07 | 6.3414e-07 | 5.1961e-07 | 4.2296e-07 | 3.424e-07 | 2.7612e-07 | 2.219e-07 | 1.7797e-07 | 1.4263e-07 | 1.1437e-07 | 9.1876e-08 | 7.4106e-08 | 6.0064e-08 | 4.9014e-08 | 4.0294e-08 | 3.3443e-08 | 2.8021e-08 | 2.3766e-08 | 2.0368e-08 | 1.7682e-08 | 1.5494e-08 | 1.3751e-08
y-velocity | 3.2982e-06 | 2.4586e-06 | 1.9507e-06 | 1.7556e-06 | 1.6839e-06 | 1.6016e-06 | 1.4833e-06 | 1.3334e-06 | 1.1749e-06 | 1.0154e-06 | 8.6344e-07 | 7.2076e-07 | 5.9964e-07 | 4.9043e-07 | 3.9763e-07 | 3.209e-07 | 2.601e-07 | 2.1567e-07 | 1.8488e-07 | 1.6623e-07 | 1.5741e-07 | 1.5404e-07 | 1.5336e-07 | 1.5501e-07 | 1.5909e-07 | 1.6226e-07 | 1.6217e-07 | 1.5883e-07 | 1.5238e-07 | 1.4409e-07 | 1.3426e-07 | 1.2243e-07 | 1.0945e-07 | 9.6113e-08 | 8.3057e-08 | 7.0774e-08 | 5.959e-08 | 4.9713e-08 | 4.1113e-08 | 3.3731e-08 | 2.7522e-08 | 2.2298e-08 | 1.8042e-08 | 1.46e-08 | 1.1843e-08 | 9.6012e-09 | 7.8087e-09 | 6.352e-09 | 5.1984e-09 | 4.2696e-09 | 3.5374e-09 | 2.942e-09 | 2.4753e-09 | 2.0962e-09 | 1.798e-09 | 1.5539e-09 | 1.3611e-09
z-velocity | 1.3878e-06 | 1.4726e-06 | 1.4374e-06 | 1.4408e-06 | 1.4205e-06 | 1.3449e-06 | 1.2297e-06 | 1.1009e-06 | 9.6105e-07 | 8.2351e-07 | 6.9692e-07 | 5.829e-07 | 4.8391e-07 | 3.9448e-07 | 3.1913e-07 | 2.5626e-07 | 2.0621e-07 | 1.7117e-07 | 1.4828e-07 | 1.3569e-07 | 1.3184e-07 | 1.3338e-07 | 1.3812e-07 | 1.4543e-07 | 1.5287e-07 | 1.5843e-07 | 1.6053e-07 | 1.5846e-07 | 1.5261e-07 | 1.4474e-07 | 1.3433e-07 | 1.2203e-07 | 1.0875e-07 | 9.5323e-08 | 8.2386e-08 | 7.0393e-08 | 5.9415e-08 | 4.97e-08 | 4.1228e-08 | 3.3988e-08 | 2.7844e-08 | 2.2721e-08 | 1.8445e-08 | 1.4912e-08 | 1.2029e-08 | 9.7042e-09 | 7.8286e-09 | 6.3245e-09 | 5.1251e-09 | 4.1678e-09 | 3.409e-09 | 2.8067e-09 | 2.333e-09 | 1.9573e-09 | 1.66e-09 | 1.4237e-09 | 1.234e-09
k | 0.99769 | 0.99524 | 0.98586 | 0.94211 | 0.77009 | 0.4625 | 0.25291 | 0.19447 | 0.15181 | 0.11153 | 0.090191 | 0.078214 | 0.072808 | 0.066238 | 0.061973 | 0.058143 | 0.0548 | 0.050969 | 0.046525 | 0.041626 | 0.036566 | 0.031613 | 0.026949 | 0.022661 | 0.01879 | 0.015372 | 0.012414 | 0.0099017 | 0.0078267 | 0.0061411 | 0.0048061 | 0.0037563 | 0.0029457 | 0.0023174 | 0.0018392 | 0.0014675 | 0.0011857 | 0.00096442 | 0.00079553 | 0.0006597 | 0.00055588 | 0.00047009 | 0.00040465 | 0.00034888 | 0.00030677 | 0.00026945 | 0.00024176 | 0.00021596 | 0.00019733 | 0.00017918 | 0.00016621 | 0.000153 | 0.00014342 | 0.00013334 | 0.0001259 | 0.00011798 | 0.00011199
omega | 0.49951 | 0.49919 | 0.49864 | 0.49763 | 0.49572 | 0.49192 | 0.48401 | 0.46719 | 0.43215 | 0.36632 | 0.26723 | 0.16101 | 0.081733 | 0.037802 | 0.017049 | 0.0078388 | 0.003794 | 0.0019814 | 0.0011318 | 0.00070808 | 0.00048157 | 0.00035023 | 0.00026762 | 0.00021234 | 0.00017344 | 0.00014511 | 0.00012377 | 0.00010715 | 9.3899e-05 | 8.3112e-05 | 7.4165e-05 | 6.6678e-05 | 6.0356e-05 | 5.4874e-05 | 5.0102e-05 | 4.5929e-05 | 4.2261e-05 | 3.9022e-05 | 3.614e-05 | 3.3562e-05 | 3.1251e-05 | 2.9175e-05 | 2.7305e-05 | 2.5608e-05 | 2.4067e-05 | 2.2662e-05 | 2.1377e-05 | 2.0183e-05 | 1.9082e-05 | 1.8064e-05 | 1.7147e-05 | 1.6335e-05 | 1.5578e-05 | 1.4869e-05 | 1.4207e-05 | 1.3581e-05 | 1.2998e-05
Table of contents
Plots / Residuals

## Slide 26
Table of contents
Plots / Report Plots
Report Plots

## Slide 27: drag_force-rplot
Chart: drag_force-rplot
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0 | 53.0 | 54.0 | 55.0 | 56.0 | 57.0
drag_force | 736.6619 | 938.9935 | 976.3854 | 930.4272 | 855.8919 | 787.6715 | 732.4756 | 696.2107 | 673.3652 | 662.1354 | 657.4007 | 657.3091 | 659.8604 | 663.4053 | 667.162 | 670.5385 | 673.2327 | 675.0103 | 676.0485 | 676.6413 | 676.9585 | 677.1011 | 677.1405 | 677.1221 | 677.0753 | 677.0189 | 676.9641 | 676.9169 | 676.8889 | 676.8559 | 676.8307 | 676.8158 | 676.8101 | 676.811 | 676.8159 | 676.8226 | 676.8294 | 676.8354 | 676.8401 | 676.8437 | 676.8463 | 676.8481 | 676.8494 | 676.8505 | 676.8514 | 676.8522 | 676.8531 | 676.854 | 676.855 | 676.856 | 676.857 | 676.858 | 676.8589 | 676.8599 | 676.8608 | 676.8617 | 676.8625
Table of contents
Plots / Report Plots / report plots

## Slide 28: lift_force-rplot
Chart: lift_force-rplot
| 1.0 | 2.0 | 3.0 | 4.0 | 5.0 | 6.0 | 7.0 | 8.0 | 9.0 | 10.0 | 11.0 | 12.0 | 13.0 | 14.0 | 15.0 | 16.0 | 17.0 | 18.0 | 19.0 | 20.0 | 21.0 | 22.0 | 23.0 | 24.0 | 25.0 | 26.0 | 27.0 | 28.0 | 29.0 | 30.0 | 31.0 | 32.0 | 33.0 | 34.0 | 35.0 | 36.0 | 37.0 | 38.0 | 39.0 | 40.0 | 41.0 | 42.0 | 43.0 | 44.0 | 45.0 | 46.0 | 47.0 | 48.0 | 49.0 | 50.0 | 51.0 | 52.0 | 53.0 | 54.0 | 55.0 | 56.0 | 57.0
lift_force | 1714.986 | 3254.7485 | 4495.0275 | 5414.9165 | 6066.7938 | 6525.5594 | 6846.346 | 7071.0566 | 7229.1954 | 7342.0724 | 7408.8495 | 7470.8306 | 7508.0534 | 7535.287 | 7556.5382 | 7571.5349 | 7582.2746 | 7590.0851 | 7594.0887 | 7595.7325 | 7596.33 | 7596.4102 | 7596.3877 | 7596.3877 | 7596.4795 | 7596.6466 | 7596.8672 | 7597.1072 | 7597.3285 | 7597.5217 | 7597.6914 | 7597.8371 | 7597.9572 | 7598.0541 | 7598.1299 | 7598.188 | 7598.2315 | 7598.2635 | 7598.287 | 7598.3044 | 7598.3179 | 7598.3289 | 7598.3385 | 7598.3475 | 7598.3562 | 7598.3646 | 7598.3729 | 7598.3808 | 7598.3883 | 7598.3951 | 7598.4014 | 7598.4069 | 7598.4118 | 7598.416 | 7598.4197 | 7598.4229 | 7598.4258
Table of contents
Plots / Report Plots / report plots